## Slide 1: PDA Lab3 OpenROAD Tutorial Advisor: Mark Po-Hung Lin TA: 吳瑞宸 林酩荏

## Slide 2: Introduction
OpenROAD is the leading open-source, foundational application for semiconductor digital design. The OpenROAD flow delivers an Autonomous, No-Human-In-Loop (NHIL) flow, 24 hour turnaround from RTL-GDSII for rapid design exploration and physical design implementation.
Doc
Github

## Slide 3: Flow

## Slide 4: Openroad
$ openroad -gui &
You can operate in tcl shell
output log
tcl command
Layout area
inst information
Display panel
- Instances
- Rows
- Heat Maps

## Slide 5: Load files (lef)

## Slide 6: Load files (def)

## Slide 7: global_placement
$ global_placement -density <value>
Value recommend from 0.8 to 0.95 depends on case

## Slide 8: extract
$ source extract.tcl
Filename: designName_insts.gp
DBU_Per_Micron 2000
DieArea_LL 83600 71820
DieArea_UR 104400 91200
Site_Width 400
Site_Height 3420
Name LLX LLY Width Height Type
inst2015 85600 78660 3200 3420 CELL
inst2591 88800 85500 4400 3420 CELL
inst2908 94800 82080 2800 3420 CELL
…

## Slide 9: detail_placement & legalization
$ detail_placement
OpenROAD would have some statistics.

## Slide 10: Cell information
The inspector shows the information such as inst_name, status, orientation, bounding box, width, height.

## Slide 11: place_cell

## Slide 12: Legality
On-site: Cells must be placed with their bottom-left corner aligned to the site grid defined by the input design data.
On-site
Illegal

## Slide 13: Legality check
$ check_placement -verbose # return 0 if pass

## Slide 14: Heatmap

## Slide 15: Heatmap Density
x0 | y0 | x1 | y1 | value
41.8 | 35.91 | 51.8 | 45.6 | 63.88235
51.8 | 35.91 | 52.2 | 45.6 | 17.64706
$ gui::dump_heatmap "Placement" “<path to csv>”

## Slide 16: Note
flow.tcl # Overall flow wrapper
extract.tcl # Extract input.gp
Please use mobaxterm to connect to the server, DO NOT use vscode ssh
  Server ip:140.113.30.188:7405
  Account: same
  Password: nycu2026